## Slide 1: Proposal to Change to Net Heat of Combustion for AAR RP-589 Locomotive Fuel Economy Calculations
Abstract – The LMOA Fuels, Lubricants, and Environment Committee recommends that RP-589 specify Net Heat of Combustion for diesel fuel heating value correction. The current specification is to use the Gross Heat of Combustion.
Background – AAR RP-589 “Rating for Specific Fuel Consumption of Diesel Electric Locomotives” is under review by a Technical Advisory Group (TAG) within the AAR Locomotive Committee.
Historically, RP-589 used the Gross Heat of Combustion (a.k.a., Higher Heating Value) for diesel fuel heating value corrections to specific fuel consumption (SFC)
Net Heat of Combustion is technically-correct SFC corrections – and is used by most other engine standards.
Current diesel fuel trends are for larger variations in hydrogen mass fraction (ULSD, biodiesel, HDRD, etc.), resulting in wider variations the difference between Gross Heat of Combustion and Net Heat of Combustion.
Conclusion – Diesel fuels used by railroads are changing and Net Heat of Combustion is a more appropriate metric to correct specific fuel consumption.
Recommendation – RP-589 should specify Net Heat of Combustion for diesel fuel heating value corrections to specific fuel consumption.
Fuel, Lube, and Environmental Committee 2018